## Slide 1: CID Flow Indicator (CIDFI, “sid fye”)
draft-wing-cidfi-03
November 16, 2023
Dan Wing, Citrix
Tiru Reddy, Nokia
Mohamed Boucadair, Orange

## Slide 2: Problem
draft-wing-cidfi-03

## Slide 3: Problem: bandwidth-constrained links (1/2)
server
client
Edge router
Wi-Fi access point
bandwidth-constrained links
router
router
router
router
router
router
draft-wing-cidfi-03

## Slide 4: Problem: different importance (2/2)
server
client
Important: keystrokes and updating screen
Less-important: file transfer
PDF file transfer
draft-wing-cidfi-03

## Slide 5: Desired Solution
Communicate packet importance within a 5-tuple to client-side bandwidth-constrained network elements
Communicate network performance information to help streams within a 5-tuple to adapt
draft-wing-cidfi-03

## Slide 6: CIDFI Overview
draft-wing-cidfi-03

## Slide 7: CIDFI Overview
Client shares flow metadata with CIDFI Network Element(s)
Optional: server can differentiate packet importance
Supports:
  Network-to-Host signaling
  Host-to-Network signaling
  Intentional and reactive management policies
  IPv6, IPv4, translation
draft-wing-cidfi-03

## Slide 8: Solution Steps
Client learns CIDFI network elements
Client requests network element participation
  Client authorizes each network element
  Each network element sends authentication token
Client connects to server (optionally CIDFI-aware)
Client sends authentication token over 5-tuple
Optional: Server sends metadata to client
Client sends CID->metadata to network elements
On network attach
Each QUIC/DTLS connection
draft-wing-cidfi-03

## Slide 9: CIDFI on one slide
server
client
Edge router (5G/DOCSIS
Wi-Fi access point
QUIC Initial, do you CIDFI?
QUIC, CIDFI=yes (data is flowing at this point)
CIDFI?
Yes, 192.168.1.1 and Edge Router’s IP
Request: do CIDFI, Response: authentication token
Request: do CIDFI, Response: authentication token
CID 1234 and 5678 are important (optional)
CID 1234 and 5678 are important
CID 1234 and 5678 are important
1.
1.
2.
3.
4.
router
router
router
router
router
router
Authentication tokens
2.
On network attach
Each QUIC/DTLS connection
draft-wing-cidfi-03

## Slide 10: CIDFI Advantages
Supports IPv4, IPv6, and IPv6/IPv4 translation
Uses QUIC v1 or DTLS Connection Id (RFC9146)
  Immutable
Internet deployable
  Only CIDFI routers, client, and server need CIDFI support
  Non-participating routers are unaffected
Metadata is extensible and does not impact QUIC packet size and MTU
draft-wing-cidfi-03

## Slide 11: CIDFI Summary
Client authorizes and coordinates signaling
  Client’s on-premise Wi-Fi and client’s ISP
Use QUIC CID or DTLS CID mapped to metadata
Signals both Network-to-Host and Host-to-Network
Optional: server differentiates packets using different CIDs
draft-wing-cidfi-03

## Slide 12: End
draft-wing-cidfi

## Slide 13: Backup

## Slide 14: 1. Client Finds Network Elements
DNS query
server
client
Edge router
router
CIDFI "cifi.arpa“ SUDN or DHCP, PvD
Yes, 192.168.1.1 and Edge Router’s IP
Network Attach

## Slide 15: 2. Client Requests Participation
server
client
Edge router
Wi-Fi access point
Let’s do CIDFI (HTTP)
router
Let’s do CIDFI (HTTP)
Network Attach
Authentication token
Authentication token

## Slide 16: 3. Client determines server supports CIDFI
New QUIC transport parameter
  remembered for 0-RTT
server
client
Edge router
Wi-Fi access point
QUIC Initial, CIDFI?
QUIC, CIDFI=yes
Network Attach

## Slide 17: 4. Server Sends CID->metadata mapping
server
client
Edge router
Wi-Fi access point
(in QUIC: CID 1234 & 5678=DSCP EF)
customer-premise network

## Slide 18: 5. Client relays mapping to network elements
server
client
Edge router
Wi-Fi access point
CID 1234 & 5678 =DSCP EF
CID 1234 & 5678 =DSCP EF
Authentication tokens

## Slide 19: Leaking Packet Importance
Concern: Recurring different CID leaks packet importance to attacker
Possible mitigations:
  Obfuscation: server maps many CIDs and retires CIDs aggressively